## Slide 1: Comparing the 2020 European Seismic Hazard Model (ESHM20) with ShakeMap Footprints: application in Greece
Nikolaos Anterriotis-Kalpakidis
&
Anastasia Kiratzi
Department of Geophysics
Aristotle University of Thessaloniki

## Slide 2
Scope – Workflow
Compare Probabilistic Seismic Hazard Assessment maps with observed data
Check their accuracy and reliability
Sources of observed Data: ShakeMap data
The 2020 European Seismic Hazard Model, ESHM20 was tested
Four (4) Aggregation levels were tested:
  Mean
  16th
  50th
  84th
Test was applied for three (3) Intensity Measures (IMs) PGA, Sa[0.3s], and Sa[1.0s]
Test was applied for a return period of 475 and 50 years
Distribution of epicenters for the final uniform catalog. The 2,617 earthquakes (Mp ≥ 4.5) are marked from the color and side scale
Build a uniform catalog for the 43,196 events in USGS ComCat from January 1973 to December 2022 [50 years]
Generate 2,617 ShakeMaps using USGS’ ShakeMap software [events with potency magnitude Mp ≥ 4.5]
Peak-motion and earthquake info (in USGS ShakeMap formats) can be retrieved via EPOS Data Portal

## Slide 3
ShakeMap Data Processing
Retrieve the maximum IMs from the ShakeMaps
- Create a 0.01°×0.01° base grid (143,728 grid cells)
- Retrieve the maximum reported IM for each grid cell
Retrieve the expected IM from the ESHM20 maps for each grid cell
Adjust soil-site ShakeMap IMs to rock site levels
Site correction
  Adjust the observed IMs to rock sites using the amplification factors of the 2020 European Seismic Risk Model, ESRM20
Observed soil-site max PGA
Adjusted rock-site max PGA
Both ShakeMaps and ESHM20 IMs are valid to RotD50

## Slide 4
Calculate Fractional Exceedance area (exceeded sites / total sites) and compare with the target
Results
Theoretical binomial distribution
Empirical distribution of the exceeded area
± 1 Std
Overlapping Coefficient (OVL) for quantitative comparison
Spatial distribution of the exceedance area

## Slide 5
Thank you for your attention
contact: nanterr@geo.auth.gr

## Slide 6: A workflow to analytically investigate seismogenic sources of historical earthquakes: new insights from Central Italy pre-instrumental seismicity V. Gironelli, L. Luzi, T. Volatili, E. Tondi
Contacts: 📩 Email: veronica.gironelli@ingv.it 🔗 LinkedIn: linkedin.com/in/veronica-gironelli-329b96210
Notes: Introduce yourself with your name, affiliation and TCS only

## Slide 7
Uncertain Historical Seismogenic sources in Central Italy
April 24, 1741:
"Fabriano earthquake"
(Imax 9 MCS; Mw 6.17)
July 28, 1799:
"Camerino earthquake"
(Imax 9-10 MCS; Mw 6.18)
November 3, 1706:
"Maiella earthquake"
(Imax 10-11 MCS; Mw 6.84)
Marche region
Abruzzi region
STUDY AREA
SH depends on expected ground motion;
Ground motion depends on the source;
Most historical earthquake source are uncertain.
How to determine the 3D historical earthquake sources?
Notes: SH  depends on ground motion;
Ground motion  controlled by the source;
Historical EQ source  often uncertain ?

## Slide 8
INPUTS
PROCESSING
OUTPUTS
1
2
3
Earthquake data (magnitude, location, depth);
Source parameters (L, W, strike, dip, rake);
Macroseismic intensity data.
GMM + Vs30 map → GMPs prediction (PGA, PGV)
GMICE → Conversion of GMPs to intensity
Residual analysis → Best source evaluation by comparing obs vs. pred intensity
SHAKING SCENARIOS in PGA – PGV - INTENSITY
MATLAB-based WORKFLOW
POSTER SESSION!