## Slide 1
11 Aprile 2013
Natural Field Laboratories as a tool for ground instabilities AI-Twins
salvatore.martino@uniroma1.it
Prof. Salvatore Martino
Perugia, 19 March 2025

## Slide 2
Salvatore Martino
Dealing with «Ground Instabilities»
Natural Field Laboratories for Ground Instabilities
Predisposing factors (geological, morphodynamic and geotechnical)
Preparatory processes (climatic actions, river dynamics, anthropic pressure)
Triggering actions (earthquakes, volcanic activity, intense rainfall, rapid melting of snow, human interventions)
TIME INDEPENDENT
CLIMATE DEPENDENT
IMPULSIVE

## Slide 3
Salvatore Martino
Concept of in-house/natural field labs
IN-HOUSE LABORATORIES include systems to "represent" site conditions in standard or prototype devices by applying principles of physical-mechanical analogy or relationships and scaling functions of site properties.
Natural Field Laboratories for Ground Instabilities
NATURAL FIELD LABORATORIES represent sites which are used for the experimentation of real-scale processes that are caused by natural or forced conditions, in both cases kept under monitoring by sensors installed on site.
Physics-Informed Neural Networks
(PINNS)
Artificial Intelligence trained Twins (AI-Twins)

## Slide 4
Salvatore Martino
Standard or Prototype devices: reality transposition
Examples of «in house» laboratories
Physic-analogue: reality transposition
Down-scaled modelling: reality reproduction
Natural Field Laboratories for Ground Instabilities

## Slide 5
Salvatore Martino
Rationale of a «natural-field» laboratory
A series of natural processes that include predisposing factors, preparatory factors and possible triggering actions are RATIONALIZED respect to a representative site….
....rationalization translates into a DESIGN that is functional in collecting, in time and space, data from the natural system and at real scale…
....this drives toward the construction of an AI-TWIN which allows projecting the expected effects in the future.
1
2
3
Natural Field Laboratories for Ground Instabilities

## Slide 6
Salvatore Martino
Toward a natural field laboratory
Concept idea
Lab design
Forward scenarios
Data analysis
AI-Twin
Data recovery
Natural Field Laboratories for Ground Instabilities

## Slide 7
Salvatore Martino
Concept idea
Lab design
Forward scenarios
Data analysis
AI-Twin
Data recovery
Natural Field Laboratories for Ground Instabilities
Toward a natural field laboratory

## Slide 8
Salvatore Martino
Ideas and their rationalization from reality
Natural Field Laboratories for Ground Instabilities
Pale di S.Martino (Dolomiti)
Monument Valley (Navaho Tribal Park – Arizona)
From observation to processes

## Slide 9
Salvatore Martino
Civita di Bagnoregio (VT)
Natural Field Laboratories for Ground Instabilities
Ideas and their rationalization from reality

## Slide 10
Salvatore Martino
~20 cm
~40 cm
Natural Field Laboratories for Ground Instabilities
Ideas and their rationalization from reality

## Slide 11
Martino, 2023
Page 11
Salvatore Martino
Natural Field Laboratories for Ground Instabilities
Ideas and their rationalization from reality
FIELD LABORATORY OBSERVATION TIME SPAN

## Slide 12
Salvatore Martino
Natural Field Laboratories for Ground Instabilities
Ideas and their rationalization from reality
FORCE DRIVEN ground instability effects
VISCOSITY DRIVEN ground instability effects

## Slide 13
Salvatore Martino
Surprise effect (???)
Natural Field Laboratories for Ground Instabilities
less than 5 minutes
Ideas and their rationalization from reality
failure

## Slide 14
Salvatore Martino
Toward a natural field laboratory
Concept idea
Lab design
Forward scenarios
Data analysis
AI-Twin
Data recovery
Natural Field Laboratories for Ground Instabilities

## Slide 15
Salvatore Martino
Create a “natural field laboratory”
https://dst.web.uniroma1.it/it/acuto-field-laboratory
https://dst.web.uniroma1.it/it/ventotene-field-laboratory
https://dst.web.uniroma1.it/it/laboratorio-naturale-di-poggio-baldi
Natural Field Laboratories for Ground Instabilities

## Slide 16
Salvatore Martino
Comune di Acuto (FR)
Prenestina Quarry (’50 of XX century)
Create a “natural field laboratory”
Natural Field Laboratories for Ground Instabilities
Today view

## Slide 17
Salvatore Martino
Equipment works at the Acuto Quarry Experimental Field (2019-2022)
Create a “natural field laboratory”
Natural Field Laboratories for Ground Instabilities

## Slide 18
Salvatore Martino
Acuto field laboratory
The actual experiments:
Block
Wall
Tower
A
B
C
Create a “natural field laboratory”
Natural Field Laboratories for Ground Instabilities

## Slide 19
Salvatore Martino
Create a “natural field laboratory”
Natural Field Laboratories for Ground Instabilities

## Slide 20
Salvatore Martino
Create a “natural field laboratory”
BLOCK
WALL
TOWER
Natural Field Laboratories for Ground Instabilities
WALL

## Slide 21
Salvatore Martino
Create a “natural field laboratory”
Natural Field Laboratories for Ground Instabilities
Historical landslide activations date back to March 1914 and March 2010. The former was a large-scale wedge failure, which was inferred by the geometric features of the scar area. The latter involved the previous landslide's body mobilizing approximately 4 million of cubic meters of material.
Corniolo Member (lower-middle Miocene)

## Slide 22
Salvatore Martino
Create a “natural field laboratory”
Data types
3D point clouds
RGB and thermal images
Noise tracks
Weather time series
Seismic data
Radar interferometry
Natural Field Laboratories for Ground Instabilities

## Slide 23
Salvatore Martino
Create a “natural field laboratory”
Natural Field Laboratories for Ground Instabilities

## Slide 24
Salvatore Martino
3D model of Punta Eolo
AFTER…
BEFORE…
Create a “natural field laboratory”
Natural Field Laboratories for Ground Instabilities

## Slide 25
Salvatore Martino
Create a “natural field laboratory”
2. DAU and Camera
1. Solar Panels
6. Rock Thermometer
10. Tide gauge
2. DAU and Camera
Natural Field Laboratories for Ground Instabilities

## Slide 26
Salvatore Martino
Create a “natural field laboratory”
Natural Field Laboratories for Ground Instabilities
22 May 2024

## Slide 27
Salvatore Martino
Toward a natural field laboratory
Concept idea
Lab design
Forward scenarios
Data analysis
AI-Twin
Data recovery
Natural Field Laboratories for Ground Instabilities

## Slide 28
Data collection and dataset construction
Natural Field Laboratories for Ground Instabilities

## Slide 29
Salvatore Martino
Data collection and dataset construction
Mastrantoni G., Santicchia G., Cosentino A., Molinari A., Marmoni G. M. & Mazzanti P. (2024). Automatic photomonitoring analysis for spatiotemporal evaluation of rockfall failure hazard. Engineering Geology, 339, https://doi.org/10.1016/j.enggeo.2024.107662
Natural Field Laboratories for Ground Instabilities
Senceive FlatMesh 4G
TimeLapse
TLA8
Mobotix S74

## Slide 30
Salvatore Martino
Data collection and dataset construction
Mastrantoni G., Santicchia G., Cosentino A., Molinari A., Marmoni G. M. & Mazzanti P. (2024). Automatic photomonitoring analysis for spatiotemporal evaluation of rockfall failure hazard. Engineering Geology, 339, https://doi.org/10.1016/j.enggeo.2024.107662
Natural Field Laboratories for Ground Instabilities
Senceive FlatMesh 4G
TimeLapse
TLA8
Automatic acquisition
Mobotix S74

## Slide 31
Salvatore Martino
Data collection and dataset construction
Natural Field Laboratories for Ground Instabilities

## Slide 32
Salvatore Martino
Data collection and dataset construction
F3
F1
F2
F4
T1
LC
Tilt
Natural Field Laboratories for Ground Instabilities

## Slide 33
Salvatore Martino
Toward a natural field laboratory
Concept idea
Lab design
Forward scenarios
Data analysis
AI-Twin
Data recovery
Natural Field Laboratories for Ground Instabilities

## Slide 34
The presence of processes involving heat propagation and phase change (e.g. freezing) in the fractured system significantly affects its vibrational response and with it its evolution towards phases of greater instability.
Grechi et al., 2023
Marmoni et al., 2020
Data analysis and results
Marmoni G.M., Fiorucci M., Grechi G., Martino S. (2020). Modelling of thermo-mechanical effects in a rock quarry wall induced by near-surface temperature fluctuations. INTERNATIONAL JOURNAL OF ROCK MECHANICS AND MINING SCIENCES, vol. 134, ISSN: 1365-1609, doi: 10.1016/j.ijrmms.2020.104440
Natural Field Laboratories for Ground Instabilities

## Slide 35
Salvatore Martino
D’Angiò et al., 2020
Data analysis and results
D’Angiò D., Fantini A., Fiorucci M., Iannucci R., Lenti L., Marmoni G.M., Martino S. (2021). Environmental forcings and micro‑seismic monitoring in a rock wall prone to fall during the 2018 Buran winter storm. NATURAL HAZARDS, vol. 106, p. 2599-2617, ISSN: 1573-0840, doi: 10.1007/s11069-021-04556-5
Natural Field Laboratories for Ground Instabilities

## Slide 36
Salvatore Martino
Data analysis and results
D’Angiò D., Fantini A., Fiorucci M., Iannucci R., Lenti L., Marmoni G.M., Martino S. (2021). Environmental forcings and micro‑seismic monitoring in a rock wall prone to fall during the 2018 Buran winter storm. NATURAL HAZARDS, vol. 106, p. 2599-2617, ISSN: 1573-0840, doi: 10.1007/s11069-021-04556-5
Natural Field Laboratories for Ground Instabilities

## Slide 37
Salvatore Martino
Source Sector | Process | Estimated Surface (m2) | Estimated Volume (m3)
Z1 | Rockfalls | 1441 | - 620
Z2 | Rockfalls | 1805 | - 475
Z3 | Rockfalls | 2795 | - 817
Z4 | Rockfalls | 1479 | - 1196
Toe | Debris accumulation | 4572 | + 5160
Robiati, C.; Mastrantoni, G.; Francioni, M.; Eyre, M.; Coggan, J.; Mazzanti, P. Contribution of High-Resolution Virtual Outcrop Models for the Definition of Rockfall Activity and Associated Hazard Modelling. Land 2023, 12, 191. https://doi.org/10.3390/land12010191
Data analysis and results
Natural Field Laboratories for Ground Instabilities

## Slide 38
Salvatore Martino
Toward a natural field laboratory
Concept idea
Lab design
Forward scenarios
Data analysis
AI-Twin
Data recovery
Natural Field Laboratories for Ground Instabilities

## Slide 39
Toward an AI-Twin
Marmoni G.M., Fiorucci M., Grechi G., Martino S. (2020). Modelling of thermo-mechanical effects in a rock quarry wall induced by near-surface temperature fluctuations. INTERNATIONAL JOURNAL OF ROCK MECHANICS AND MINING SCIENCES, vol. 134, ISSN: 1365-1609, doi: 10.1016/j.ijrmms.2020.104440
Natural Field Laboratories for Ground Instabilities

## Slide 40
Toward an AI-Twin
Thermo-mechanical modelling
Thermal modelling
Marmoni G.M., Fiorucci M., Grechi G., Martino S. (2020). Modelling of thermo-mechanical effects in a rock quarry wall induced by near-surface temperature fluctuations. INTERNATIONAL JOURNAL OF ROCK MECHANICS AND MINING SCIENCES, vol. 134, ISSN: 1365-1609, doi: 10.1016/j.ijrmms.2020.104440
Natural Field Laboratories for Ground Instabilities

## Slide 41
Salvatore Martino
Numerical modelling through finite difference element method
Toward an AI-Twin
Natural Field Laboratories for Ground Instabilities

## Slide 42
Salvatore Martino
Sea level
Thermo-mechanical approach
Toward an AI-Twin
Daily thermal input
Monthly thermal input
Yearly thermal input
Natural Field Laboratories for Ground Instabilities

## Slide 43
Salvatore Martino
Toward an AI-Twin
Average Sea Wave of 2 m and 6s of period
Natural Field Laboratories for Ground Instabilities

## Slide 44
Salvatore Martino
Toward a natural field laboratory
Concept idea
Lab design
Forward scenarios
Data analysis
AI-Twin
Data recovery
Natural Field Laboratories for Ground Instabilities

## Slide 45
Salvatore Martino
Scenarios of ground instability effects in a forward perspective
Natural Field Laboratories for Ground Instabilities

## Slide 46
Salvatore Martino
Scenarios of ground instability effects in a forward perspective
Mastrantoni, G., Santicchia, G., Cosentino, A., Molinari, A., Marmoni, G. M., & Mazzanti, P. (2024). Automatic photomonitoring analysis for spatiotemporal evaluation of rockfall failure hazard. Engineering Geology, 339, 107662
Natural Field Laboratories for Ground Instabilities

## Slide 47
Salvatore Martino
Mastrantoni, G., Santicchia, G., Cosentino, A., Molinari, A., Marmoni, G. M., & Mazzanti, P. (2024). Automatic photomonitoring analysis for spatiotemporal evaluation of rockfall failure hazard. Engineering Geology, 339, 107662
Scenarios of ground instability effects in a forward perspective
Natural Field Laboratories for Ground Instabilities

## Slide 48
Salvatore Martino
Training an ANN for prediction using machine learning approaches of inelastic event scenarios (wall block detachments)
Training
Prediction
% (ep>erange)
0 (em In range)
1 (em Out of Range)
Probability
(e≠ erange)
The neural network has 50 neurons in the hidden layer, the «ReLU» (Rectified Linear unit) function is used as the transfer function
The output layer is a "softmax layer", where the outputs are normalized to probability values ​​proportional to the exponential of the input values.
The network is trained by minimizing the "cross entropy loss function" through the Broyden-Fletcher-Goldfarb-Shanno quasi-Newton algorithm (LBFGS).
To limit the overfitting effect, we adopted the "early stop by validation" training criterion.
Scenarios of ground instability effects in a forward perspective
Natural Field Laboratories for Ground Instabilities

## Slide 49
Salvatore Martino
Local weather dataset (100 nets)
Scenarios of ground instability effects in a forward perspective
Natural Field Laboratories for Ground Instabilities

## Slide 50
Salvatore Martino
Scenarios of ground instability effects in a forward perspective
Air Force-provided weather data (100 nets)
Natural Field Laboratories for Ground Instabilities

## Slide 51
Salvatore Martino
Really occurred event at Castrocielo on 21 /11/2023
Scenarios of ground instability effects in a forward perspective
Natural Field Laboratories for Ground Instabilities

## Slide 52
Salvatore Martino
….to conclude
Concept idea
Lab design
Forward scenarios
Data analysis
AI-Twin
Data recovery
The aim of the NATURAL FIELD LABORATORIES within the current lines of research and which perspective for risk mitigation strategies consists in supporting the creation of tools for the generation of scenarios of ground instability effects. However, the knowledge base represented by datasets deriving from monitoring systems already operational for years can represent a product that can be transferred into the EPOS project
Natural Field Laboratories for Ground Instabilities

## Slide 53
Salvatore Martino
Thanks for your attention
salvatore.martino@uniroma1.it
11 Aprile 2013
Natural Field Laboratories for Ground Instabilities