## Slide 1: Advanced Geochemical Monitoring Integrated with Geophysical Observations in Seismic Zones of Japan
Hirochika SUMINO
Research Center for Advanced Science and Technology,
The University of Tokyo, JAPAN

## Slide 2: Core Monitoring Networks: Seismic and Geodetic Foundations
Hi-net (1995), S-net (2017), DONET (2011), N-net (2025) by NIED ‒ ~800 inland borehole stations and ~200 offshore station network continuously monitoring microearthquake activity with high sensitivity
GEONET (GNSS Earth Observation Network) by GSI (1994) – >1,300 continuous GNSS stations providing fundamental data for tracking crustal strain and the accumulation of elastic strain energy
Hi-net
GEONET
NIED = National Research Institute for Earth Science and Disaster Prevention
GSI = Geospatial Information Authority of Japan
S-net, DONET, & N-net

## Slide 3: Real-Time Response and Rapid Modeling
REGARD (Real-time GEONET Analysis system for Rapid Deformation) by GSI (2016) – provide real-time finite fault models for M≥7 earthquakes using 1Hz GNSS data
SGDAS (Seismic Ground Disaster Assessment System) by GSI (2019) – rapid landslide and liquefaction assessment
Example: 2024 Noto Peninsula earthquake (M7.6) 6 sec. The first Earthquake Early Warning was announced by JMA 4 min. REGARD successfully estimated a fault model, aiding in immediate initial response and tsunami predictions 8 min. SGDAS completed a map of potential ground hazards (slope collapses and liquefaction) 10 min. Fault models and regional crustal deformation data were automatically distributed to the relevant agencies
JMA = Japan Meteorological Agency

## Slide 4: Major Inland Earthquakes During the Past ~30 Years
Hanshin-Awaji
M7.3 (1995)
West. Tottori
M7.3 (2000)
Chuetsu
M6.8 (2004)
Noto
M6.9 (2007) M7.5 (2024)
Iwate-Miyagi
M7.2 (2008)
North. Nagano
M6.7 (2014)
Kumamoto
M7.3 (2016)
North. Osaka
M6.1 (2018)
Hokkaido East. Iburi
M6.7 (2018)
Active fault zones everywhere = difficulty with multidisciplinary and permanent near-fault observatories
Active Fault Database by GSJ (2005) – organizes faults by "behavioral segments" based on rupture history and surface geometry
Rupture Probability Map by GSJ (2005) – based on the Cascade Earthquake Model for risk assessment
Active fault zones (red), other faults (black) and probability of IJMA≥6-lower in 30 years
GSJ = Geological Survey of Japan

## Slide 5: Noto Peninsula Earthquakes
Feb 7, 1993: M6.6
Mar 25, 2007: M6.9
2018~: Earthquake swarm begins
2020~: Earthquake swarm intensifies
Jun 19, 2022: M5.4
May 5, 2023: M6.5
Jan 1, 2024: M7.6 mainshock (Devastating damage, tsunami, over 200 fatalities)
M6.6 (1993)
M6.9 (2007)
Before 2018
2018-2023
2024
M7.6

## Slide 6: 3He/4He of hot springs in the Noto Peninsula
High mantle contributions in SUZU and WAJIMA.
Moderate mantle contributions near active faults.

## Slide 7: Multidisciplinary Observations Reveal Origin/Role of Fluids
Consistent with the distribution of deep-derived fluids inferred from seismic tomography. (Nakajima, EPS 2022)
Earthquakes occurred where the low S wave velocity anomaly seems connected to the mantle, and high 3He/4He were observed.  triggered by the ascent of deep- derived fluids
Black and grey dots: earthquake hypocenters, red circles: M ≥ 5
H
I
J
Fluids
SUZU
WAJIMA
A
B
A
B

## Slide 8: Temporal 3He/4He Variations as Precursory Signal
Two hot springs in SUZU showed a decrease in 3He/4He before the 2024 M7.6 mainshock, which may have resulted from the addition of radiogenic helium (4He) degassed from the aquifer rocks.
This may reflect the volumetric strain change on the bedrock and can be regarded as a precursor to the mainshock.
(Kagoshima et al., Nature Commun. 2025)

## Slide 9: Conventional 3He/4He analysis and problems
Helium is generally rare in a volcanic gas sample (1–100 ppm).
  removal of active gases and noble gas separation (particularly Ar) are required.
    Noble gas purification and separation line is necessary.
3He is even more scarce. 3He/4He = 10−7–10−5  3He in the ppt order
HD+ (D: deuterium) is an interference of 3He+ detection.
  High sensitivity and high mass resolution are required.
    A magnetic-sector mass spectrometer is generally used.
Purification and separation line
weight：~1 t
~2 m
Magnetic-sector mass spectrometer
Samples are analyzed after being taken back to the laboratory.
Real-time and continuous measurement is quite difficult.
All the previous 3He/4He variations were identified after the eruptions.
A portable mass spectrometer and a compact helium extraction system are necessary.
Notes: まず，ヘリウムは天然試料中の存在度が非常に小さく，ガス試料であれば1–100 ppm程度しか存在しません。
そのため，分析には，窒素や酸素など活性ガスの除去と，希ガス元素ごと分離，特にヘリウムと比べて大気中に1000倍以上存在するアルゴンの分離が必要となります。
これには，金属のゲッターや活性炭トラップを含む希ガス精製ラインが用いられます。
さらに，ヘリウムの同位体の中でも3Heは特に微量で，全試料中だとpptオーダーしか存在しません。
また，重水素を含むHD+は3He+の妨害イオンとなります。
そのため，同位体比の測定には，微量の3Heを検出できるだけの高い感度と，3HeとHDを識別できるだけの質量分解能が必要となります。
その要件を満たす分析計としては，磁場型質量分析計が用いられています。
これらの設備を持ち運ぶのはほぼ不可能なため，火山ガスのヘリウム同位体比の測定は，現地でサンプリングを行った後，試料を実験室に持ち帰って行うことになります。
したがって，防災への利用に不可欠な，リアルタイム・連続観測は現在の手法では困難です。
これを解決するには，可搬型の質量分析計とコンパクトなヘリウム抽出システムを用いた，オンサイト分析の手法が必要となります。

## Slide 10: A portable mass spectrometer
Multi-turn time-of-flight mass spectrometer (MULTUM)[5]–[7]
Ions are focused into a closed orbit flight path.
Small and lightweight (52 × 63 × 35 cm，48 kg including pumping system)
Resolution > 30,000 (theoretically infinite)
[5] Toyoda et al., J. Mass Spectrom. (2000). [6] Okumura et al., J. Mass Spectrom. Soc. Jpn. (2003). [7] Shimma et al., Anal. Chem. (2010).
63 cm
52 cm
35 cm
weight：48 kg
Chart: 3He/4He by Magnetic-Sector MS [RA]
| 6.9603109248510657 | 5.652120347633776 | 7.6993698480457962 | 7.9188652147023761 | 7.6145365398412084 | 1
 | 6.591 | 5.7539 | 7.4524 | 7.3985 | 7.3196 | 0.93
 | 6.9603 | 5.6521 | 7.6994 | 7.9189 | 7.6145 | 1
Error bars are 1 sigma.
1:1
Sensitivity improved by 5k times
First 3He detection with a portable instrument
The standard sample size (50 mL) is enough to obtain 3He/4He.
Despite lower precision than conventional instruments, pre-eruptive 3He/4He variations are expected to be detected.
Notes: 可搬型の質量分析計として，我々はマルチターン飛行時間型質量分析計，通称MULTUMを採用しました。
これは飛行時間型質量分析計の一種で，８の字の飛行経路でイオンを周回させ，質量分析計ごとの飛行時間の差によってイオンを分離し，質量スペクトルを得る分析計です。
一般的な飛行時間型質量分析計では，まっすぐの飛行経路でイオンを質量分離しますが，MULTUMでは飛行経路を電場制御によって８の字に曲げることで，サイズを小さく保ったまま高い質量分解能を実現しています。
そのため，小型・軽量で十分に持ち運びが可能であり，3HeとHDを十分に識別できるだけの質量分解能を有しています。
ただし，感度については天然試料中の微量の3Heを検出するのに必要な水準に遠く及びませんでした。
したがって，MULTUMを用いてヘリウム同位体比を測定するためには，感度を向上させて，3Heの検出および定量を可能にすることが課題でありました。

## Slide 11: Summary and Future Perspective
Although geophysical (seismological and geodetic) monitoring has been intensively carried out in Japan, “ubiquitous” faults hinder the establishment of a multidisciplinary and permanent near-fault observatory.
Nevertheless, advanced geochemical studies using helium isotopes have shown their significance for understanding deep fluid migration causing earthquakes and detecting precursory signals.
To realize continuous on-site 3He/4He monitoring, the development of portable instruments is ongoing.
MoU between the relevant universities/institutes running NFOs in EPOS and Univ. Tokyo
Application to bilateral funds between the relevant agencies in EU countries and JSPS (Japan Society for the Promotion of Science)
are planned to promote the exchange of monitoring techniques and young researchers between NFO and the Japanese community.
for the international collaborations…

## Slide 13: Long-Term Risk Assessment and Databases
Active Fault Database by GSJ (2005) – organizes faults by "behavioral segments" based on rupture history and surface geometry
Rupture Probability Map by GSJ (2005) – based on the Cascade Earthquake Model, which assesses the probability that segments will rupture individually or in conjunction with neighbors, for infrastructure planning and risk assessment
Active fault zones (red), other faults (black) and probability of IJMA≥6-lower in 30 years
GSJ = Geological Survey of Japan

## Slide 14: Major Inland Earthquakes During the Past ~30 Years
Hanshin-Awaji
M7.3 (1995)
West. Tottori
M7.3 (2000)
Chuetsu
M6.8 (2004)
Noto
M6.9 (2007) M7.5 (2024)
Iwate-Miyagi
M7.2 (2008)
North. Nagano
M6.7 (2014)
Kumamoto
M7.3 (2016)
North. Osaka
M6.1 (2018)
Hokkaido East. Iburi
M6.7 (2018)
Active fault zones everywhere = difficulty with establishing (permanent) near-fault observatories

## Slide 15: Earthquake Early Warning (EEW)
緊急地震速報 (Kinkyu Jishin Sokuho)
(JMA = Japan Meteorological Agency)
http://www.jma.go.jp/jma/en/Activities/eew.html
Video (10 min.)

## Slide 16: Advanced Geodetic Techniques for Interseismic Strain
InSAR and GNSS Integration: combination of satellite-based InSAR with GNSS data to overcome challenges in forested or steep terrain
Example at Atotsugawa Fault System: detailed interseismic velocity fields were revealed, and sharp velocity gradients across major strands like the Ushikubi fault, which were previously difficult to map with high spatial resolution, were identified
(Takada et al., EPS 2018)
Atotsugawa
Ushikubi

## Slide 17: Hot Spring Sampling Sites and 3He/4He Analysis
weight：~1 t
~2 m
Magnetic-sector mass spectrometer
Preparation line

## Slide 18: What Does Helium Isotope Ratio Tell?
Chemically inert, thus reflects mixing ratios of several components with different origins
Relative contributions in He from Mantle / Crust / Air
Air contribution can be corrected based on 4He/20Ne Air- corrected 3He/4He  Mantle / Crust
Mantle-derived
(Sano & Wakita, JGR 1985)
Crust-derived
Geothermal fluids in Japan
3He/4He

## Slide 19: Comparison with Geophysical Observations (2)
High 3He/4He were associated with the boundary between high and low gravity anomaly, the latter of which in the northeastern Noto Peninsula is interpreted as a Miocene caldera (Yamazaki and Kono, Bull. Volcanon. Soc. Jpn. 1973).  fluid migration along caldera wall?
Bouguer gravity anomaly

## Slide 20: Deep Structure and Fluid Migration
2.3 RA
0.02 RA
6.8 RA
4.3 RA
SUZU
WAJIMA
A
B
In WAJIMA on the northwestern Noto Peninsula, where deep-derived fluids ascended and triggered the 2007 M6.9 earthquake and subsequent swarms, the fluids reached the surface via active faults.
In SUZU on the northeastern Noto Peninsula, the deep-derived fluid reached the surface via the caldera wall.

## Slide 21: A portable mass spectrometer
Multi-turn time-of-flight mass spectrometer (MULTUM)[5]–[7]
Ions are focused into a closed orbit flight path.
Small and lightweight (52 × 63 × 35 cm，48 kg including pumping system)
Resolution > 30,000 (theoretically infinite if the ions remained in the flight path)
Sensitivity is not high enough to detect 3He in natural samples.
[5] Toyoda et al., J. Mass Spectrom. (2000). [6] Okumura et al., J. Mass Spectrom. Soc. Jpn. (2003). [7] Shimma et al., Anal. Chem. (2010).
Analyzer
Detector
Ion source
Shimma et. al. (2010)
63 cm
52 cm
35 cm
weight：48 kg
Improvement in sensitivity to detect 3He is necessary for 3He/4He analysis.
Notes: 可搬型の質量分析計として，我々はマルチターン飛行時間型質量分析計，通称MULTUMを採用しました。
これは飛行時間型質量分析計の一種で，８の字の飛行経路でイオンを周回させ，質量分析計ごとの飛行時間の差によってイオンを分離し，質量スペクトルを得る分析計です。
一般的な飛行時間型質量分析計では，まっすぐの飛行経路でイオンを質量分離しますが，MULTUMでは飛行経路を電場制御によって８の字に曲げることで，サイズを小さく保ったまま高い質量分解能を実現しています。
そのため，小型・軽量で十分に持ち運びが可能であり，3HeとHDを十分に識別できるだけの質量分解能を有しています。
ただし，感度については天然試料中の微量の3Heを検出するのに必要な水準に遠く及びませんでした。
したがって，MULTUMを用いてヘリウム同位体比を測定するためには，感度を向上させて，3Heの検出および定量を可能にすることが課題でありました。

## Slide 22: Analyses of volcanic gas samples with modified MULTUM
The data obtained with MULTUM are consistent with those obtained with a conventional mass spectrometer within 1σ errors.
Chart: 3He/4He by Magnetic-Sector MS [RA]
| 6.9603109248510657 | 5.652120347633776 | 7.6993698480457962 | 7.9188652147023761 | 7.6145365398412084 | 1
 | 6.591 | 5.7539 | 7.4524 | 7.3985 | 7.3196 | 0.93
 | 6.9603 | 5.6521 | 7.6994 | 7.9189 | 7.6145 | 1
Error bars are 1 sigma.
1:1
Pulse counting of detector signals to improve S/N ratio
Static mode operation to keep sample gas in the mass spectrometer
Improved ion transmission
Sensitivity improved by 5000 times!
First 3He detection with a portable instrument
The standard sample size (50 mL) is enough to obtain 3He/4He.
Despite lower precision than conventional instruments, pre-eruptive 3He/4He variations are expected to be detected.
Detectable!
Notes: 最後に，MULTUMによる火山ガス試料の測定結果になります。
5つの火山ガス試料の3He/4He比をMULTUMを用いて測定しました。
グラフの横軸は磁場型質量分析計による測定値で，縦軸がMULTUMによる測定値を表します。
MULTUMによる測定値は，同じ試料の磁場型質量分析計による測定値とおよそ1σのの範囲内で一致するという結果が得られました。
以上がMULTUMに関する開発概要と評価結果になります。

## Slide 23: On-board He isotope analysis
JAMSTEC
Yokosuka YK23-16S Cruise (2023. 9. 15-29)
K. Tani (NMNS), Chief Scientist

## Slide 24: On-board He isotope analysis
First on-board 3He/4He data!
He sensitivity decreases with high Ar/He due to suppression of He ionization.
3He
HD

## Slide 25: Variations in Helium Isotope Ratios in Hot Spring Water and Groundwater Before and After the 2024 Noto Peninsula Earthquake
Collaboration with: Miyu HASEGAWA, Koji UMEDA Hirosaki University, Japan
Noritoshi MORIKAWA
Geological Survey of Japan, AIST, Japan