## Slide 1
Notes: Good morning everybody
First of all thank you very much for coming
I am very happy that a lot of people are interested in this topic
So, just few words about the structure of this workshop
We will have the first part, a little bit of theory but not so much formulas or something like that
We will go straight on the processing on the Distributed environment, I will show you the services developed by me and my team on GPOD and GEP platform
You will have also the possibility to ask questions
I am Claudio De Luca and I come from the Institute of Electromagnetic Sensing of Environment (IREA)
We work since a long time on RADAR data acquired by satellites and we work basically on SAR Interferometry that is the technique that I will go to explain you
That permits us to detect the ground deformation of the Earth surface

## Slide 2
Active sensors
Microwave sensors
Coherent sensors
Key points of Radar (SAR) Imaging from space

## Slide 3
Passive sensors use solar radiation (light) or the one emitted by the observed object as source of illumination. Typically they operate in the optical or infrared.
Active sensors have their own source of illumination. Typically they operate in the microwave.
Capability to "observe" during day and night
Key points of Radar (SAR) Imaging from space

## Slide 4
Optical image
Radar (SAR) image
same moment of acquisition
Capability to "observe" even in presence of clouds
Key points of Radar (SAR) Imaging from space

## Slide 5
Coherent sensors
SAR image
Synthetic Aperture
Key points of Radar (SAR) Imaging from space
Notes: Another important aspect of the as said before is that the radar is coherent
The coherence is a concept that came from the phisics that is related to the optical interferometry and subsequently trasled in the radar field
What means coherent? It means that you have a sensor, you have a transmitted signal and you know exactly the signal, in particula the phase of your signal
In this slide I show you a radar moving on the orbital path, sending a signal and reciving it along the path. At the end you can combine all these recived signals along the
Lenght of the Synthetic Aperture.

## Slide 6: Differential SAR Interferometry (DInSAR)
SAR Image @ t0

## Slide 7
SAR Image @ t1
Baseline
SAR Image @ t0
Differential SAR Interferometry (DInSAR)

## Slide 8
Ground Displacement
(Amatrice Earthquake - 24/08/2016)
Displacement [cm]
> 20
< - 20
Differential SAR Interferometry (DInSAR)

## Slide 9
VOLCANIC
SEISMIC
URBAN
LANDSLIDES
DInSAR can play a key role in many contexts

## Slide 10
Observations are done at different epochs and from different orbital positions (real case)
Topographic Phase
Deformation Phase
LOS: Line Of Sight
Differential SAR Interferometry (DInSAR)
Notes: 10

## Slide 11
DInSAR
Interferogram
Generation
(Flattening)
Coherence
Map
Topographic
Interferogram
(DEM & orbital
information are
needed)
15042009_20052009_bperp=20m
Differential SAR Interferometry (DInSAR)

## Slide 12
Campi Flegrei (3-7/2000)
π
π
Centimetric displacements (in some cases even sub-centimetric) can be measured in “coherent” areas!
ERS wavelenght: 5.6 cm
Differential SAR Interferometry (DInSAR)
-

## Slide 13
Studying Earthquakes with DInSAR
Landers earthquake, 1992 was the first interferogram of an earthquake using ERS images.
Co-seismic interferogram using ERS data (92/4/24-93/6/18).

## Slide 14
Phase Interpretation

## Slide 15
0
2.8
cm
40°30’ N
Astroni
Solfatara
Arco Felice
Agnano
Bagnoli
3/2000-7/2000
Phase Unwrapping Operation
Wrapped Phase (-π, π)
Differential SAR Interferometry (DInSAR)

## Slide 16
PhU: Phase Unwrapping
p
- p
rad
Wrapped Phase
PhU
4
- 27
cm
Unwrapped Phase
Notes: Aquila 2009

## Slide 17
ground motion
(relative to the satellite)
cm
0 cm
/2 cm
away from
towards
pass 1
pass 2
Initial ground surface
Subsided ground surface
phase
difference
The Interferometric Phase (interpretation)

## Slide 18
Fringe analysis
2.8
0
[cm]
Sentinel-1: 21082016–27082016
C-band:
= 5.5 cm
Descending

## Slide 19
Fringe analysis
8
-21
[cm]
Sentinel-1: 21082016–27082016
C-band:
= 5.5 cm
Descending

## Slide 20
Fringe analysis
2.8
0
[cm]
Sentinel-1: 15082016–27082016
C-band:
= 5.5 cm
Ascending

## Slide 21
5
-22
[cm]
Sentinel-1: 15082016–27082016
C-band:
= 5.5 cm
Ascending
Fringe analysis

## Slide 22
Fringe analysis

## Slide 23
A
.33.97N
44.29E
35.33N
46.60E
π
- π
rad
0
30
80 km
B
LOS displacement (cm)
> 89
-89 <
0
30
80 km
.33.97N
44.29E
35.33N
46.60E
Fringe analysis

## Slide 24
Multi-orbit LOS displacement combination
Asc
Desc
θ
East
z
P

## Slide 25
Ascending Orbit
Descending Orbit
Multi-orbit LOS displacement combination

## Slide 26
ALOS-2 ASC (09092015 – 24082016)
ALOS-2 DESC (25052016 – 31082016)
Sentinel-1 DESC (21082016 – 27082016)
<-20 >20
LOS Deformation [cm]
Sentinel-1 ASC (15082016 – 27082016)
Amatrice earthquake (24/08/2016): DInSAR analysis

## Slide 27
> 20
< - 20
[cm]
Up
Down
< - 20
> 20
[cm]
East
West
Amatrice earthquake: Vertical and East-West components

## Slide 28
Etna summit eruption and Fiandaca Earthquake
Sentinel-1 descending orbits: 22 – 28 december 2018
Azimuth

## Slide 29
Azimuth
Cm
cm
>10
<-10
Etna summit eruption and Fiandaca Earthquake
Sentinel-1 descending orbits: 22 – 28 december 2018

## Slide 30
Azimuth
Etna summit eruption and Fiandaca Earthquake
Sentinel-1 ascending orbits: 16 – 28 december 2018

## Slide 31
Cm
cm
>10
<-10
Azimuth
Etna summit eruption and Fiandaca Earthquake
Sentinel-1 ascending orbits: 16 – 28 december 2018

## Slide 32
Vertical component
Cm
cm
>10
<-10
Up
Down

## Slide 33
East-West component
Cm
cm
>30
<-30
East
West

## Slide 34
Different Atmospheric Conditions from one image to another lead to artifacts in the generated interferograms. Such effects can be reduced by properly averaging independent interferograms (stacking).
DInSAR Limitations

## Slide 35
Mt. Etna – Sentinel-1 Descending Orbit: 15.02.2021 – 21.02.2021
Azimuth
Baseline Perp. 92m
Cm
rad
+π
-π
DInSAR Limitations: atmospheric conditions

## Slide 36
Azimuth
Mt. Etna – Sentinel-1 Descending Orbit: 15.02.2021 – 27.02.2021
DInSAR Limitations: atmospheric conditions
Baseline Perp. 5m
Cm
rad
+π
-π

## Slide 37
Azimuth
Baseline Perp. 98m
Cm
rad
+π
-π
Mt. Etna – Sentinel-1 Descending Orbit: 21.02.2021 – 27.02.2021
DInSAR Limitations: atmospheric conditions

## Slide 38
Baseline Perp. 43m
Azimuth
Mt. Etna – Sentinel-1 Ascending Orbit: 15.02.2021 – 27.02.2021
DInSAR Limitations: atmospheric conditions
Cm
rad
+π
-π

## Slide 39
Baseline Perp. 0.3m
Azimuth
Mt. Etna – Sentinel-1 Ascending Orbit: 21.02.2021 – 27.02.2021
DInSAR Limitations: atmospheric conditions
Cm
rad
+π
-π

## Slide 40
N
Azimuth
31.08.2019 – 06.09.2019
06.09.2019 – 12.09.2019
12.09.2019 – 18.09.2019
2.8
0
cm
Stromboli – Sentinel-1 Descending Orbit
DInSAR Limitations: atmospheric conditions

## Slide 41
N
Azimuth
18.09.2019 – 24.09.2019
2.8
0
cm
24.09.2019 – 30.09.2019
Stromboli – Sentinel-1 Descending Orbit
DInSAR Limitations: atmospheric conditions
12.10.2019 – 18.10.2019

## Slide 42
21.01.2021 – 03.02.2021
28.01.2021 – 09.02.2021
N
N
2.8
0
cm
2.8
0
cm
03.02.2021 – 15.02.2021
N
2.8
0
cm
Azimuth
Stromboli – Sentinel-1 Descending Orbit
DInSAR Limitations: atmospheric conditions
Atmospheric artefacts are typically not correlated in time!

## Slide 43
ERS1_01/05/1996 - ERS2_15/08/1996 baseline=950 m
ERS2_31/08/1995 - ERS2_ 15/08/1996 baseline=10 m
Napoli Bay (ERS Multi-look image)
DInSAR Limitations
Spatial Decorrelation Effects depend on the perpendicular baseline of the used SAR data pairs. To reduce such effects the use of small spatial baseline couples is required.
Notes: 43

## Slide 44
Temporal Decorrelation Effects are due to temporal reflectivity changes of the imaged scene. Such effects can be mitigated by using small temporal baselines or long wavelength signals.
Possible causes of reflectivity changes:
Vegetation
Meteorology (snow, ice, …)
Eruptions (erupted material deposit, lava flows, …)
Fires
Hydrogeology (floods, landslides, sinkholes, …)
Anthropogenic (building construction/demolition, …)
…
DInSAR Limitations

## Slide 45
Mt. Etna – Sentinel-1 Descending Orbit
DInSAR Limitations: temporal decorrelation
Cm
rad
+π
-π
14.05.2018 – 20.05.2018
14.05.2018 – 13.06.2018
14.05.2018 – 11.10.2018
N
N
N
6 days
36 days
150 days

## Slide 46
N
20 Jun 2019 – 26 Jun 2019
Azimuth
26 Jun 2019 – 8 Jul 2019
8 Juò 2019 – 14 Jul 2019
Pre-event
Co-event
Post-event
Stromboli, 3rd July 2019 paroxysm – Sentinel-1 Descending Orbit
DInSAR Limitations: temporal decorrelation

## Slide 47
N
Azimuth
20 Jun 2019 – 26 Jun 2019
26 Jun 2019 – 8 Jul 2019
8 Juò 2019 – 14 Jul 2019
Pre-event
Co-event
Post-event
Stromboli, 3rd July 2019 paroxysm – Sentinel-1 Descending Orbit
DInSAR Limitations: temporal decorrelation

## Slide 48
Baseline Perp. 5m
Azimuth
SEC
Cm
1
0
Pre-event
Mt. Etna – Sentinel-1 Ascending Orbit: 28.01.2021 – 09.02.2021
DInSAR Limitations: temporal decorrelation

## Slide 49
Azimuth
SEC
~4 km
Co-event
Mt. Etna – Sentinel-1 Ascending Orbit: 03.02.2021 – 21.02.2021
DInSAR Limitations: temporal decorrelation
Baseline Perp. 26m
Cm
1
0

## Slide 50
Thank you!
monterroso.f@irea.cnr.it